## Slide 1: Ch2-2 How to improve the performance of Memory hierarchy

## Slide 2: Memory Technology and Optimizations
Performance metrics
  Latency is concern of cache
  Bandwidth is concern of multiprocessors and I/O
  Access time
    Time between read request and when desired word arrives
  Cycle time
    Minimum time between unrelated requests to memory
SRAM memory has low latency, use for cache
Organize DRAM chips into many banks for high bandwidth, use for main memory

## Slide 3: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refeshed
    Every ~ 8 ms (roughly 5% of time)
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)

## Slide 4: DRAM logical organization (64 Mbit)
Square root of bits per RAS/CAS
Column Decoder
Sense
Amps & I/O
Memory
Array
(16,384×16,384)
A0…A1
3
…
Address buffer
14
Data in
D
Q
Word Line
Storage
Cell
Data out
Row Decoder
…
Bit Line

## Slide 5: DRAM Read Timing
Every DRAM access begins at:
  The assertion of the RAS_L
  2 ways to read: early or late v. CAS
A
D
OE_L
256K x 8
DRAM
9
8
WE_L
CAS_L
RAS_L
OE_L
A
Row Address
WE_L
Junk
Read Access
Time
Output Enable
Delay
CAS_L
RAS_L
Col Address
Row Address
Junk
Col Address
D
High Z
Data Out
DRAM Read Cycle Time
Early Read Cycle: OE_L asserted before CAS_L
Late Read Cycle: OE_L asserted after CAS_L
Junk
Data Out
High Z
Notes: Similar to DRAM write, DRAM read can also be a Early read or a Late read.
In the Early Read Cycle, Output Enable is asserted before CAS is asserted so the data lines will contain valid data one Read access time after the CAS line has gone low.
In the Late Read cycle, Output Enable is asserted after CAS is asserted so the data will not be available on the data lines until one read access time after OE is asserted.
Once again, notice that the RAS line has to remain asserted during the entire time. The DRAM read cycle time is defined as the time between the two RAS pulse.
Notice that the DRAM read cycle time is much longer than the read access time.
Q: RAS & CAS at same time? Yes, both must be low
+2 = 65 min. (Y:45)

## Slide 6: Internal Organization of DRAM

## Slide 7: Times of fast and slow DRAMs with each generation.

## Slide 8: Memory Optimizations

## Slide 9: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device

## Slide 10: 1st Improving DRAM Performance Fast Page Mode DRAM (FPM)
Timing signals that allow repeated accesses to the row buffer (page) without another row access time
Such a buffer comes naturally, as each array will buffer 1024 to 2048 bits for each access.
Page: All bits on the same ROW (Spatial Locality)
  Don’t need to wait for wordline to recharge
  Toggle CAS with new column address

## Slide 11: 2nd Improving DRAM Performance Synchronous DRAM
conventional DRAMs have an asynchronous interface to the memory controller, and hence every transfer involves overhead to synchronize with the controller.
The solution was to add a clock signal to the DRAM interface, so that the repeated transfers would not bear that overhead.
  Data output is in bursts w/ each element clocked

## Slide 12: 3rd Improving DRAM Performance DDR--Double data rate
On both the rising edge and falling edge of the DRAM clock signal, DRAM innovation to increase bandwidth is to transfer data,
  thereby doubling the peak data rate.
2.5V
1.8v
1.5v

## Slide 13: DDR--Double data rate
DDR:
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1333 MHz
GDDR5 is graphics memory based on DDR3

## Slide 14: 4rd Improving DRAM Performance New DRAM Interface: RAMBUS (RDRAM)
a type of synchronous dynamic RAM, designed by the Rambus Corporation.
Each chip has interleaved memory and a high speed interface.
Protocol based RAM w/ narrow (16-bit) bus
  High clock rate (400 Mhz), but long latency
  Pipelined operation
Multiple arrays w/ data transferred on both edges of clock
The first generation RAMBUS interface dropped RAS/CAS, replacing it with a bus that allows other accesses over the bus between the sending of the address and return of the data. It is typically called RDRAM.
The second generation RAMBUS interface include a separate row- and column-command buses instead of the conventional multiplexing; and a much more sophisticated controller on chip. Because of the separation of data, row, and column buses, three transactions can be performed simultaneously. called Direct RDRAM or DRDRAM

## Slide 15: RDRAM Timing

## Slide 16: RAMBUS (RDRAM)
RAMBUS Bank
RDRAM Memory System

## Slide 17: Comparing RAMBUS and DDR SDRAM
Since the most computers use memory in DIMM packages, which are typically at least 64-bits wide, the DIMM memory bandwidth is closer to what RAMBUS provides than you might expect when just comparing DRAM chips.
Caution that performance of cache are based in part on latency to the first byte and in part on the bandwidth to deliver the rest of the bytes in the block.
  Although these innovations help with the latter case, none help with latency.
  Amdahl’s Law reminds us of the limits of accelerating one piece of the problem while ignoring another part.

## Slide 18: Memory Optimizations
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketted DIMM modules

## Slide 19: Summery
Memory organization
  Wider memory
  Simple interleaved memory
  Independent memory banks
  Avoiding Memory Bank Conflicts
Memory chip
  Fast Page Mode DRAM
  Synchronize DRAM
  Double Date Rate
  RDRAM

## Slide 20: Memory Power Consumption

## Slide 21: Stacked/Embedded DRAMs
Stacked DRAMs in same package as processor
  High Bandwidth Memory (HBM)

## Slide 22: Flash Memory
Type of EEPROM
Types: NAND (denser) and NOR (faster)
NAND Flash:
  Reads are sequential, reads entire page (.5 to 4 KiB)
  25 us for first byte, 40 MiB/s for subsequent bytes
  SDRAM: 40 ns for first byte, 4.8 GB/s for subsequent bytes
  2 KiB transfer: 75 uS vs 500 ns for SDRAM, 150X slower
  300 to 500X faster than magnetic disk

## Slide 23: NAND Flash Memory
Must be erased (in blocks) before being overwritten
Nonvolatile, can use as little as zero power
Limited number of write cycles (~100,000)
$2/GiB, compared to $20-40/GiB for SDRAM and $0.09 GiB for magnetic disk
Phase-Change（相变）/Memrister Memory
  Possibly 10X improvement in write performance and 2X improvement in read performance

## Slide 24: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  Use spare rows to replace defective rows
Chipkill: a RAID-like error recovery technique

## Slide 25: How to Improve Cache Performance?
Reduce hit time(4)
  Small and simple first-level caches, Way prediction
  avoiding address translation, Trace cache
Increase bandwidth(3)
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty(5)
  multilevel caches, read miss prior to writes,
  Critical word first, merging write buffers, and victim caches
Reduce miss rate(4)
  larger block size, large cache size, higher associativity
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization (1)
  Hardware or compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 26: 1st Hit Time Reduction Technique: Small and Simple Caches
Using small and Direct-mapped cache
The less hardware that is necessary to implement a cache, the shorter the critical path through the hardware.
Direct-mapped is faster than set associative for both reads and writes.
Fitting the cache on the chip with the CPU is also very important for fast access times.

## Slide 27: L1 Size and Associativity
Access time vs. size and associativity

## Slide 28: L1 Size and Associativity
Energy per read vs. size and associativity

## Slide 29: 2nd Hit Time Reduction Technique: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty

## Slide 30: 2nd Hit Time Reduction Technique: Way Prediction
Way Prediction (Pentium 4 )
  Extra bits are kept in the cache to predict the way,or block within set of the next cache access.
  If the predictor is correct, the instruction cache latency is 1 clock clock cycle.
  If not,it tries the other block, changes the way predictor, and has a latency of 1 extra clock cycles.
  Simulation using SPEC95 suggested set prediction accuracy is excess of 85%, so way prediction saves pipeline stage in more than 85% of the instruction fetches.

## Slide 31: 3rd Hit Time Reduction Technique: Avoiding Address Translation during Indexing of the Cache
Page table is a large data structure in memory
TWO memory accesses for every load, store, or instruction fetch!!!
Virtually addressed cache?
  synonym problem
Cache the address translations?
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data

## Slide 32: TLBs
A way to speed up translation is to use a special cache of recently used page table entries -- this has many names, but the most frequently used is Translation Lookaside Buffer or TLB
Virtual Address Physical Address Dirty Ref Valid Access
Really just a cache on the page table mappings
TLB access time comparable to cache access time
(much less than main memory access time)

## Slide 33: Translation Look-Aside Buffers
Just like any other cache, the TLB can be organized as fully associative, set associative, or direct mapped
TLBs are usually small, typically not more than 128 - 256 entries even on high end machines. This permits fully associative lookup on these machines. Most mid-range machines use small n-way set associative organizations.
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB

## Slide 34: Fast hits by Avoiding Address Translation
CPU
TB
$
MEM
VA
PA
PA
Conventional
Organization
CPU
$
TB
MEM
VA
VA
PA
Virtually Addressed Cache
Translate only on miss
Synonym Problem
VA
Tags
CPU
$
TB
MEM
VA
PA
Tags
PA
Virtual indexed, Physically tagged
Overlap $ access
with VA translation:
requires $ index to
remain invariant
across translation
L2 $

## Slide 35: Virtual Addressed Cache
Send virtual address to cache? Called Virtually Addressed Cache or
just Virtual Cache (vs. Physical Cache)
Every time process is switched logically must flush the cache; otherwise get false hits
  Cost is time to flush + “compulsory” misses from empty cache
  Add process identifier tag that identifies process as well as address within process: can’t get a hit if wrong process
Any Problems ?

## Slide 36: Virtual cache

## Slide 37: Dealing with aliases
Dealing with aliases (synonyms); Two different virtual addresses map to same physical address
NO aliasing! What are the implications?
HW antialiasing: guarantees every cache block has unique address
    verify on miss (rather than on every hit)
    cache set size <= page size ?
    what if it gets larger?
How can SW simplify the problem? (called page coloring)
  I/O must interact with cache, so need virtual address

## Slide 38: Aliases problem with Virtual cache
If the index and offset bits of two aliases are forced to be
the same, than the aliases address will map to the same block in cache.

## Slide 39: Overlap address translation and cache access (Virtual indexed, physically tagged)
Any limitation ?

## Slide 40: What’s the limitation?
IF it’s direct map cache, then
Cache size = 2index * 2blockoffset <= 2 pageoffset
How to solve this problem?
Use higher association. Say it’s a 4 way, then cache size can reach 4 times 2pageoffset with change nothing in index or tag or offset.

## Slide 41: Example: Virtual indexed, physically tagged cache
VPN: 30bits 8bits 5bits
=
=
VA
V D 25 bits 256 bits
V D 25 bits 256 bits
bank0
bank1
0
0
255
255
V D 30 bits 25 bits
=
=
=
=
VPN PPN
Cache
PPN：25bits
index block offset
TLB
Virtual address wide = 43 bits, Memory physical address wide = 38 bits, Page size = 8KB.
Cache capacity =16KB. If a virtually indexed and physically tagged cache is used.
And the cache is 2-way associative write back cache with 32 byte block size.

## Slide 42: 4th Hit Time Reduction Technique: Trace caches
Find a dynamic sequence of instructions including taken branches to load into a cache block.
The block determined by CPU instead of by memory layout.
Complicated address mapping mechanism

## Slide 43: Why Trace Cache ?
Bring N instructions per cycle
  No I-cache misses
  No prediction miss
  No packet breaks !
  Because branch in each 5 instruction, so cache can only provide a packet in one cycle.

## Slide 44: What’s Trace ?
Trace: dynamic instruction sequence
When instructions ( operations ) retire from the pipeline, pack the instruction segments into TRACE, and store them in the TRACE cache, including the branch instructions.
Though branch instruction may go a different target, but most times the next operation sequential will just be the same as the last sequential. ( locality )

## Slide 45: Whose propose ?
Peleg Weiser (1994) in Intel corporation
Patel / Patt ( 1996)
Rotenberg / J. Smith (1996)
Paper: ISCA’98

## Slide 46: Trace in CPU

## Slide 47: Instruction segment

## Slide 48: Pentium 4: trace cache, 12 instr./per cycle

## Slide 49: How to Improve Cache Performance?
Reduce hit time(4)
  Small and simple first-level caches, Way prediction
  avoiding address translation, Trace cache
Increase bandwidth(3)
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty(5)
  multilevel caches, read miss prior to writes,
  Critical word first, merging write buffers, and victim caches
Reduce miss rate(4)
  larger block size, large cache size, higher associativity
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization (1)
  Hardware or compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 50: Pipelined Caches
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity

## Slide 51: 1st Increasing cache bandwidth: Pipelined Caches
Hit in multiple cycles,
giving fast clock cycle time

## Slide 52: 2nd Increasing cache bandwidth: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Banking works best when accesses naturally spread themselves across banks  mapping of addresses to banks affects behavior of memory system
Interleave banks according to block address,Simple mapping that works well is “sequential interleaving”

## Slide 53
Single banked two bank two bank two bank
consecutive interleaving group interleaving

## Slide 54: 3rd Increasing cache bandwidth: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss” ， “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty
Nonblocking, in conjunction with out-of-order execution, can allow the CPU to continue executing instructions after a data cache miss.

## Slide 55: How to Improve Cache Performance?
Reduce hit time(4)
  Small and simple first-level caches, Way prediction
  avoiding address translation, Trace cache
Increase bandwidth(3)
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty(5)
  multilevel caches, read miss prior to writes,
  Critical word first, merging write buffers, and victim caches
Reduce miss rate(4)
  larger block size, large cache size, higher associativity
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization (1)
  Hardware or compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 56: 1st Miss Penalty Reduction Technique: Multilevel Caches
This method focuses on the interface between the cache and main memory.
Add an second-level cache between main memory and a small, fast first-level cache, to make the cache fast and large.
The smaller first-level cache is fast enough to match the clock cycle time of the fast CPU and to fit on the chip with the CPU, thereby lessening the hits time.
The second-level cache can be large enough to capture many memory accesses that would go to main memory, thereby lessening the effective miss penalty.

## Slide 57: Parameter about Multilevel cache
The performance of a two-level cache is calculated in a similar way to the performance for a single level cache.
L2 Equations
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1
Miss PenaltyL1 = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2
AMAT = Hit TimeL1 +
Miss RateL1 x (Hit TimeL2 + Miss RateL2 * Miss PenaltyL2)
So the miss penalty for level 1 is calculated using the hit time, miss rate, and miss penalty for the level 2 cache.

## Slide 58: Two conceptions for two-level cache
Definitions:
  Local miss rate— misses in this cache divided by the total number of memory accesses to this cache (Miss rateL2)
  Global miss rate—misses in this cache divided by the total number of memory accesses generated by the CPU
Using the terms above, the global miss for the first-level cache is stall just Miss rateL1, but for the second-level cache it is :

## Slide 59: 2nd Miss Penalty Reduction Technique: Giving Priority to Read Misses over Writes
If a system has a write buffer, writes can be delayed to come after reads.
The system must, however, be careful to check the write buffer to see if the value being read is about to be written.

## Slide 60: Write buffer
Write-back want buffer to hold displaced blocks
  Read miss replacing dirty block
  Normal: Write dirty block to memory, and then do the read
  Instead copy the dirty block to a write buffer, then do the read, and then do the write
  CPU stall less since restarts as soon as do read
Write-through want write buffers => RAW conflicts with main memory reads on cache misses
  If simply wait for write buffer to empty, might increase read miss penalty (old MIPS 1000 by 50% )
  Check write buffer contents before read; if no conflicts, let the memory access continue

## Slide 61: 3nd Miss Penalty Reduction Technique: Critical Word First & Early Restart
Don’t wait for full block to be loaded before restarting CPU
  Critical Word First—Request the missed word first from memory and send it to the CPU as soon as it arrives; let the CPU continue execution while filling the rest of the words in the block. Also called wrapped fetch and requested word first
  Early restart—As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
Generally useful only in large blocks,
Spatial locality => tend to want next sequential word, so not clear if benefit by early restart

## Slide 62: Example: Critical Word First
Assume:
cache block＝64-byte
L2: take 11 CLK to get the critical 8 bytes,(AMD Athlon)
and then 2 CLK per 8 byte to fetch the rest of the
block
There will be no other accesses to rest of the block
Calculate the average miss penalty for critical word first.
Then assuming the following instructions read data sequentially 8 bytes at a time from the rest of the block
Compare the times with and without critical word first.

## Slide 63: 4th Miss Penalty Reduction Technique: Merging write Buffer
One word writes replaces with multiword writes, and it improves buffers’s efficiency.
In write-through ,When write misses if the buffer contains other modified blocks,the addresses can be checked to see if the address of this new data matches the address of a valid write buffer entry.If so,the new data are combined with that entry.
The optimization also reduces stalls due to the write buffer being full.

## Slide 64: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
No write buffering
Write buffering

## Slide 65: 5th Miss Penalty Reduction Technique: Victim Caches
A victim cache is a small (usually, but not necessarily) fully-associative cache that holds a few of the most recently replaced blocks or victims from the main cache.
This cache is checked on a miss data before going to next lower-level memory(main memory).
  to see if they have the desired item
  If found, the victim block and the cache block are swapped.
  The AMD Athlon has a victim caches (write buffer for write back blocks ) with 8 entries.

## Slide 66: The Victim Cache

## Slide 67: How to combine victim Cache ?
How to combine fast hit time of direct mapped yet still avoid conflict misses?
Add buffer to place data discarded from cache
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 68: How to Improve Cache Performance?
Reduce hit time(4)
  Small and simple first-level caches, Way prediction
  avoiding address translation, Trace cache
Increase bandwidth(3)
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty(5)
  multilevel caches, read miss prior to writes,
  Critical word first, merging write buffers, and victim caches
Reduce miss rate(4)
  larger block size, large cache size, higher associativity
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization (1)
  Hardware or compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 69: Where misses come from?
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. Also called cold start misses or first reference misses. (Misses in even an Infinite Cache)
  Capacity—If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses in Fully Associative Size X Cache)
  Conflict—If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision misses or interference misses. (Misses in N-way Associative, Size X Cache)
4th “C”:
  Coherence - Misses caused by cache coherence.
Notes: Intuitive Model by Mark Hill

## Slide 70: 3Cs Absolute Miss Rate (SPEC92)

## Slide 71: 3Cs Relative Miss Rate
Flaws: for fixed block size
Good: insight => invention

## Slide 72: Reducing Cache Miss Rate
To reduce cache miss rate, we have to eliminate some of the misses due to the three C's.
We cannot reduce capacity misses much except by making the cache larger.
We can, however, reduce the conflict misses and compulsory misses in several ways:

## Slide 73: Cache Organization?
Assume total cache size not changed:
What happens if:
Change Block Size:
Change Associativity:
3) Change Compiler:
Which of 3Cs is obviously affected?
Notes: Ask which affected?
Block size
1) Compulsory
2) More subtle, will change mapping

## Slide 74: 1st Miss Rate Reduction Technique: Larger Block Size (fixed size&assoc)
Larger blocks decrease the compulsory miss rate by taking advantage of spatial locality.
Drawback--curve is U-shaped
  However, they may increase the miss penalty by requiring more data to be fetched per miss.
  In addition, they will almost certainly increase conflict misses since fewer blocks can be stored in the cache.
  And maybe even capacity misses in small caches
Trade-off
  Trying to minimize both the miss rate and the miss penalty.
  The selection of block size depends on both the latency and bandwidth of lower-level memory

## Slide 75: Miss Rate relates Block size
Block size | Cache size |  |  | 
 | 4K | 16K | 64K | 256K
16 | 8.57% | 3.94% | 2.04% | 1.09%
32 | 7.24% | 2.87% | 1.35% | 0.70%
64 | 7.00% | 2.64% | 1.06% | 0.51%
128 | 7.78% | 2.77% | 1.02% | 0.49%
256 | 9.51% | 3.29% | 1.15% | 0.49%

## Slide 76: Performance curve is U-shaped
Reduced
compulsory
misses
Increased
Conflict
Misses
What else drives up block size?

## Slide 77: Example: Larger Block Size (C-26)
Assume: memory takes 80 clock cycles of overhead and then delivers 16 bytes every 2 cycles.
1 clock cycle hit time independent of block size.
Which block size has the smallest AMAT for each size in Fig.5.17 ?
Answer:
  AMAT16-byte block, 4KB = 1+(8.57%*82)=8.027
  AMAT256-byte block, 256KB= 1+(0.49%*112)=1.549

## Slide 78: 2nd Miss Rate Reduction Technique: Larger Caches
rule of thumb: 2 x size => 25% cut in miss rate
What does it reduce ?
Cache Size

## Slide 79: Pro. Vs. cons for large caches
Pro.
  Reduce capacity misses
Con.
  Longer hit time, Higher cost, AMAT curve is U-shaped
Popular in off-chip caches
Block size | Miss penalty | Cache size |  |  | 
 |  | 4K | 16K | 64K | 256K
16 | 82 | 8.027 | 4.231 | 2.673 | 1.894
32 | 84 | 7.082 | 3.411 | 2.134 | 1.588
64 | 88 | 7.160 | 3.323 | 1.933 | 1.449
128 | 96 | 8.469 | 3.659 | 1.979 | 1.470
256 | 112 | 11.651 | 4.685 | 2.288 | 1.549

## Slide 80: 3rd Miss Rate Reduction Technique: Higher Associativity
Conflict misses can be a problem for caches with low associativity (especially direct-mapped).
With higher associativity decreasing Conflict misses to improve miss rate
cache rule of thumb
2:1 rule of thumb a direct-mapped cache of size N has the same miss rate as a 2-way set-associative cache of size N/2.
Eight-way set associative is for practical purposes as effective in reducing misses for these sized cache as fully associative.

## Slide 81: Associativity
Conflict
2:1 rule of thumb

## Slide 82: Associativity vs Cycle Time
Beware: Execution time is only final measure!
Why is cycle time tied to hit time?
Will Clock Cycle time increase?
  Hill [1988] suggested hit time for 2-way vs. 1-way external cache +10%, internal + 2%
  suggested big and dumb caches

## Slide 83: AMAT vs. Miss Rate (P430)
Example: assume CCT = 1.36 for 2-way, 1.44 for 4-way, 1.52 for 8-way vs. CCT direct mapped
Cache Size Associativity
(KB) 1-way 2-way 4-way 8-way
4 3.44 3.25 3.22 3.28
8 2.69 2.58 2.55 2.62
16 2.33 2.40 2.46 2.53
32 2.06 2.30 2.37 2.45
64 1.92 2.24 2.18 2.25
128 1.52 1.84 1.92 2.00
256 1.32 1.66 1.74 1.82
512 1.20 1.55 1.59 1.66
(Red means A.M.A.T. not improved by more associativity)

## Slide 84: 4th Miss Rate Reduction Technique: Compiler Optimizations
The techniques reduces miss rates without any hardware changes and reorders instruction sequence with compiler.
Instructions
  Reorder procedures in memory so as to reduce conflict misses
  Profiling to look at conflicts(using tools they developed)
Data
  Merging Arrays: improve spatial locality by single array of compound elements vs. 2 arrays
  Loop Interchange: change nesting of loops to access data in order stored in memory
  Loop Fusion: Combine 2 independent loops that have same looping and some variables overlap
  Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows

## Slide 85: Merging Arrays
Combining independent matrices into a single compound array.
Improving spatial locality
Example
  /*before*/
  Int val[SIZE];
  Int key[SIZE];
  /*after*/
  Struct merge{
  int val;
  int key;
  }
  Struct merge merged_array[SIZE]

## Slide 86: b. Loop Interchange
/* Before */
for (k = 0; k < 100; k = k+1)
for (j = 0; j < 100; j = j+1)
for (i = 0; i < 5000; i = i+1)
x[i][j] = 2 * x[i][j];
/* After */
for (k = 0; k < 100; k = k+1)
for (i = 0; i < 5000; i = i+1)
for (j = 0; j < 100; j = j+1)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words;
By switching the order in which loops execute, misses can be reduced due to improvements in spatial locality.

## Slide 87: c. Loop fusion
By fusion the code into a single loop, the data that are fetched into the cache can be used repeatedly before being swapped out.
Imporving the temporal locality
Example:
/*before*/ /*after*/
For (i=0; i<N; i=i+1) For (i=0; i<N; i=i+1)
For (i=0; j<N; j=i+1) For (j=0; j<N; j=i+1)
a[i][j]=1/b[i][j]*c[i][j]; {
For (i=0; i<N; i=i+1)
a[i][j]=1/b[i][j]*c[i][j];
For (j=0; j<N; j=j+1) d[i][j]=a[i][j]*c[i][j];
d[i][j]=a[i][j]*c[i][j]; }

## Slide 88: d. Unoptimized Matrix Multiplication
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{r = 0;
for (k = 0; k < N; k = k+1)
r = r + y[i][k]*z[k][j];
x[i][j] = r;
};
Two Inner Loops:
  Write N elements of 1 row of X[ ]
  Read N elements of 1 row of Y[ ] repeatedly
  Read all NxN elements of Z[ ]
Capacity Misses a function of N & Cache Size:
  2N3 + N2 => (assuming no conflict; otherwise …)
Idea: compute on BxB submatrix that fits
y[1][k]
z[k][j]
x[1][j]
((N+N)N+N)N=2N3 + N2
Accessed For N3 operations

## Slide 89: Blocking optimized Matrix Multiplication
Matrix multiplication is
performed by multiplying the
submatrices first.
/* After */
for (jj = 0; jj < N; jj = jj+B)
for (kk = 0; kk < N; kk = kk+B)
for (i = 0; i < N; i = i+1)
for (j = jj; j < min(jj+B-1,N); j = j+1)
{r = 0;
for (k = kk; k < min(kk+B-1,N); k = k+1)
r = r + y[i][k]*z[k][j];
x[i][j] = x[i][j] + r;
};
Y benefits from spatial locality
Z benefits from temporal locality
Capacity Misses from 2N3 + N2 to N3/B+2N2
BN
B×B
BN
(BN+BN)+B2)×(N/B)2=2N3/B + N2
Accessed For N3 operations
B called Blocking Factor

## Slide 90: Reducing Conflict Misses by Blocking
Conflict misses in caches not FA vs. Blocking size
  Lam et al [1991] a blocking factor of 24 had a fifth the misses vs. 48 despite both fit in cache

## Slide 91: Summary of Compiler Optimizations to Reduce Cache Misses (by hand)

## Slide 92: 5th Miss Rate Reduction Technique: Way Prediction and Pseudo-Associative Cache
Using two Technique reduces conflict misses and yet maintains hit speed of direct-mapped cache
  Predictive bit - Pseudo-Associative
Way Prediction (Alpha 21264 )
  Extra bits are kept in the cache to predict the way,or block within set of the next cache access.
  If the predictor is correct, the instruction cache latency is 1 clock clock cycle.
  If not,it tries the other block, changes the way predictor, and has a latency of 3 clock cycles.
  Simulation using SPEC95 suggested set prediction accuracy is excess of 85%, so way prediction saves pipeline stage in more than 85% of the instruction fetches.

## Slide 93: Pseudo-Associative Cache (column associative)
How to combine fast hit time of Direct Mapped and have the lower conflict misses of 2-way SA cache?
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit (slow hit)
Drawback: CPU pipeline is hard if hit takes 1 or 2 cycles
  Better for caches not tied directly to processor (L2)
  Used in MIPS R1000 L2 cache, similar in UltraSPARC
Time
Hit Time
Pseudo Hit Time
Miss Penalty

## Slide 94: Pseudo-Associative Cache

## Slide 95: How to Improve Cache Performance?
Reduce hit time(4)
  Small and simple first-level caches, Way prediction
  avoiding address translation, Trace cache
Increase bandwidth(3)
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty(5)
  multilevel caches, read miss prior to writes,
  Critical word first, merging write buffers, and victim caches
Reduce miss rate(4)
  larger block size, large cache size, higher associativity
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization (1)
  Hardware or compiler prefetching
AMAT = HitTime + MissRateMissPenalty

## Slide 96: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Pentium 4 Pre-fetching

## Slide 97: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining

## Slide 98: Use HBM to Extend Hierarchy
128 MiB to 1 GiB
Smaller blocks require substantial tag storage
Larger blocks are potentially inefficient
One approach (L-H):
  Each SDRAM row is a block index
  Each row contains set of tags and 29 data segments
  29-set associative
  Hit requires a CAS

## Slide 99: Use HBM to Extend Hierarchy
Another approach (Alloy cache):
  Mold tag and data together
  Use direct mapped
Both schemes require two DRAM accesses for misses
  Two solutions:
    Use map to keep track of blocks
    Predict likely misses

## Slide 100: Use HBM to Extend Hierarchy

## Slide 101: Summary

## Slide 102: 1st Miss Penalty/Rate Reduction Technique: Hardware Prefetching of Inst.and data
The act of getting data from memory before it is actually needed by the CPU.
This reduces compulsory misses by retrieving the data before it is requested.
Of course, this may increase other misses by removing useful blocks from the cache.
  Thus, many caches hold prefetched blocks in a special buffer until they are actually needed.
E.g., Instruction Prefetching
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in “stream buffer”
  On miss check stream buffer
Prefetching relies on having extra memory bandwidth that can be used without penalty

## Slide 103: 2nd Miss Penalty/Rate Reduction Technique: Compiler-controlled prefetch
The compiler inserts prefetch instructions to request the data before they are needed
Data Prefetch Load data into register (HP PA-RISC loads)
  Cache Prefetch: load into cache (MIPS IV, PowerPC, SPARC v. 9)
  Special prefetching instructions cannot cause faults; a form of speculative execution
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Can be incorrect. Faults?
Issuing Prefetch Instructions takes time
  Is cost of prefetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 104: Example (P307): Compiler-controlled prefetch
for( i=0; i <3; i = i +1)
for( j=0; j<100; j=j+1)
a[i][j] = b[j][0] * b[j+1][0];
16B/block， 8B/element， 2elements/block
A[i][j]: 3*100 the even value of j will miss,
the odd values will hit, total 150 misses
B[i][j]：101*3 the same elements are accessed for each iteration of i
j=0 B[0][0]、B[1][0] 2
j=1 B[1][0]、B[2][0] 1
total 2+99=101 misses

## Slide 105: Example cont.: Compiler-controlled prefetch
For (j=0; j<100; j=j+1){
Prefetch(b[j+7][0]);
prefetch(a[0][j+7]);
a[0][j]=b[j][0]*b [j+1][0];}; 7 misses for b
4 misses for a
For (I=1; I<3; I=I+1)
For (j=0; j<100; j=j+1){
prefetch(a[i][j+7]);
a[i][j]=b[j][0]*b [j+1][0];};4 misses for a[1][j]
4 misses for a[2][j]
Total: 19 misses
save 232 cache misses at the price of 400 prefetch instructions.

## Slide 106
End.